## Slide 1: Procesamiento de Vídeo Digital
Grado en Ingeniería de Tecnologías de Telecomunicación
Imágenes de alto rango dinámico
Javier Mateos Delgado
jmd@decsai.ugr.es

## Slide 2: Exposición (recordatorio)
Exposición: cantidad de luz que recibe el sensor para que se forme una imagen.
Subexposición: La cantidad de luz es insuficiente para ver con perfección.
Sobrexposición: La cantidad de luz es demasiada para poder ver con perfección.
Mecanismos de control de la exposición:
Tiempo de exposición
Apertura del diafragma
Sensibilidad ISO
Lectura recomendada: Curso de fotografía digital http://www.thewebfoto.com

## Slide 3: La cámara (recordatorio)
escena
sensor
lente
Círculo de confusión
[http://hyperphysics.phy-astr.gsu.edu/hbasees/geoopt/lenseq.html]

## Slide 4: La cámara (recordatorio)

## Slide 5: High Dynamic Range Images
Slides from Paul Debevec and Alexei A. Efros
Notes: http://www.flickr.com/photos/artiephotography/3513060620/

## Slide 6: Problem: Dynamic Range
1500
1
25,000
400,000
2,000,000,000
The real world is high dynamic range.

## Slide 7: Long Exposure
10-6
106
10-6
106
Real world
Picture
0 to 255
High dynamic range

## Slide 8: Short Exposure
10-6
106
10-6
106
Real world
Picture
High dynamic range
0 to 255

## Slide 9
pixel (312, 284) = 42
Image
42 photons?
Notes: 2

## Slide 10: Camera Calibration
Geometric
  How pixel coordinates relate to directions in the world
Radiometric
  How pixel values relate to radiance amounts in the world
Notes: Today, we are concerned with radiometric calibration.
James: Photometric vs. radiometric -> Debevec and Malik discuss this a little in paragraph 3 of Section 2.1.
http://www.pauldebevec.com/Research/HDR/debevec-siggraph97.pdf

## Slide 11: Camera Calibration
Geometric
  How pixel coordinates relate to directions in the world in other images.
Radiometric
  How pixel values relate to radiance amounts in the world in other images.
Notes: What we will estimate is actually a relative value of the radiance up to a scale factor.

## Slide 12: The Image Acquisition Pipeline
Scene
radiance
(W/sr/m )
Lens
2
Watts per steradian per square meter
Radiance: Radiant flux (power) emitted, reflected, transmitted or received by a given surface per unit solid angle.
Solid angle
Measured in steradians
This is a directional quantity. (Often called ‘intensity’ – confusing.)
Notes: 3
Note: Response of the lens to scene radiance is not strictly linear – glass reflects some light, some light is blocked, etc.
Solid angle: https://en.wikipedia.org/wiki/Solid_angle

## Slide 13: The Image Acquisition Pipeline
Scene
radiance
(W/sr/m )
ò
Sensor
exposure
Lens
Shutter
2
Dt
Sensor
irradiance
(W/m )
2
Irradiance: Radiant flux (power) received by a surface per unit area. Not directional (collected at surface). (Often called ‘intensity’ – great, also confusing.)
Notes: 3

## Slide 14: The Image Acquisition Pipeline
Scene
radiance
(W/sr/m )
ò
Sensor
exposure
Lens
Shutter
2
Dt
Analog
voltages
Digital
values
Pixel
values
ADC
Remapping
CCD
Raw Image
JPEG Image
Sensor
irradiance
(W/m )
2
Notes: 3

## Slide 15: Varying Exposure
Notes: Memorial church, Stanford.
No image is satisfying as none capture the sense of place that we would see when visiting.

## Slide 16: What do we see?
Vs.

## Slide 17: Camera is not a photometer!
Limited dynamic range
  Perhaps use multiple exposures?
Unknown, nonlinear response
  Not possible to convert pixel values to radiance
Solution:
  Recover response curve from multiple exposures, then reconstruct the radiance map
Notes: 4

## Slide 18: Camera is not a photometer!
Key observation:
  We do not know the absolute value of exposure at each pixel.
  Assume scene is static.
  We know that the scene radiance remains constant across an image sequence.
Notes: 4

## Slide 19: Recovering High Dynamic Range Radiance Maps from Photographs
Paul Debevec
Jitendra Malik
August 1997
Computer Science Division
University of California at Berkeley
Notes: 1

## Slide 20: Ways to vary exposure
Shutter Speed (*)
F/stop (aperture, iris)
Neutral Density (ND) Filters

## Slide 21: Shutter Speed
Ranges: Canon D30: 30 to 1/4,000 sec.
Sony VX2000: ¼ to 1/10,000 sec.
Pros:
Directly varies the exposure
Usually accurate and repeatable
Issues:
Noise in long exposures

## Slide 22: Shutter Speed
Note: shutter times usually obey a power series – each “stop” is a factor of 2
¼, 1/8, 1/15, 1/30, 1/60, 1/125, 1/250, 1/500, 1/1000 sec
Usually really is:
¼, 1/8, 1/16, 1/32, 1/64, 1/128, 1/256, 1/512, 1/1024 sec

## Slide 23: Why not the aperture or ND filters?
Varying aperture changes depth of field.
Image content changes.
ND filters are inconvenient and time consuming to put on.
Likely to move camera -> breaks static scene

## Slide 24: Setup
1. Take set of exposures with varying shutter speed Dt
2. Scene is static, so radiance is fixed
3. Know pixel values output
4. Assume camera response curve is non-linear but monotonic
Notes: 10
g() is the unknown discrete inverse response function.
Zij is the known (but noisy) pixel value from 0 to 255 for location i in image j.
Ei is the unknown radiance at location i.
Δtj is the known exposure time, e.g. 1/16, 1/125, etc. for image j

## Slide 25: The Algorithm
• 3
• 1
• 2
Dt = 1 sec
• 3
• 1
• 2
Dt = 1/16 sec
• 3
• 1
• 2
Dt = 4 sec
• 3
• 1
• 2
Dt = 1/64 sec
Image series
• 3
• 1
• 2
Dt = 1/4 sec
Exposure = Radiance × Dt
log Exposure = log Radiance + log Dt
Pixel Value Z = f (Exposure)
Notes: 10
g() is the unknown discrete inverse response function.
Zij is the known (but noisy) pixel value from 0 to 255 for location i in image j.
Ei is the unknown radiance at location i.
Δtj is the known exposure time, e.g. 1/16, 1/125, etc. for image j

## Slide 26
log Exposure = log (Radiance × Dt)
Imaging system response function f
Pixel
value
0
255
(CCD photon count)
f monotonically increasing -> invertible
Notes: 1
is this curve sloped the wrong way? Isn’t more detail given to darker regions? No it’s correct because the x axis is log scale.

## Slide 27: The Algorithm
• 3
• 1
• 2
Dt = 1 sec
• 3
• 1
• 2
Dt = 1/16 sec
• 3
• 1
• 2
Dt = 4 sec
• 3
• 1
• 2
Dt = 1/64 sec
Image series
• 3
• 1
• 2
Dt = 1/4 sec
ln Exposure
Assuming unit radiance
for each pixel
Pixel value
3
1
2
Notes: 10

## Slide 28
Response Curve
ln Exposure
Assuming unit radiance
for each pixel
After adjusting radiances to obtain a smooth response curve
Pixel value
3
1
2
ln Exposure
Pixel value

## Slide 29: The Algorithm
• 3
• 1
• 2
Dt = 1 sec
• 3
• 1
• 2
Dt = 1/16 sec
• 3
• 1
• 2
Dt = 4 sec
• 3
• 1
• 2
Dt = 1/64 sec
Image series
• 3
• 1
• 2
Dt = 1/4 sec
ln Exposure = ln Radiance + ln Dt
ln Exposure
Assuming unit radiance
for each pixel
Pixel value
3
1
2
Exposure = Radiance x Dt
Pixel Value Z = f(Exposure)
f -1(Pixel Value Z) = Radiance x Dt
ln f -1(Pixel Value Z) = ln(Radiance) + ln(Dt)
Notes: 10

## Slide 30: The Math
Let g(z) be the discrete inverse response function
For each pixel site i in each image j, want:
Solve the overdetermined linear system:
fitting term
N = # pixels P = # images
g = ln f -1
g(Pixel Value ) = ln() + ln(D)

## Slide 31: The Math
Let g(z) be the discrete inverse response function
For each pixel site i in each image j, want:
Solve the overdetermined linear system:
fitting term
smoothness term
N = # pixels P = # images
g’’ = second derivative
= amount of smoothing
g = ln f -1
g(Pixel Value ) = ln() + ln(D)
is noisy! Add smoothing

## Slide 32: Matlab Code
function [g,lE]=gsolve(Z,B,l,w)
n = 256;
A = zeros(size(Z,1)*size(Z,2)+n+1,n+size(Z,1));
b = zeros(size(A,1),1);
k = 1; %% Include the data-fitting equations
for i=1:size(Z,1)
for j=1:size(Z,2)
wij = w(Z(i,j)+1);
A(k,Z(i,j)+1) = wij; A(k,n+i) = -wij; b(k,1) = wij * B(i,j);
k=k+1;
end
end
A(k,129) = 1; %% Fix the curve by setting its middle value to 0
k=k+1;
for i=1:n-2 %% Include the smoothness equations
A(k,i)=l*w(i+1); A(k,i+1)=-2*l*w(i+1); A(k,i+2)=l*w(i+1);
k=k+1;
end
x = A\b; %% Solve the system using SVD
g = x(1:n);
lE = x(n+1:size(x,1));

## Slide 33: Results: Monochromatic Digital Camera
Recovered response curve
log Exposure
Pixel value
Kodak DCS460 1/30 to 30 sec
Notes: 13
Kodak DCS460 is a ‘digital camera back’ – a sensor and processor attached to an existing camera and lens system.
6MP sensor.
Kodak DCS460 also came in a color variant - Kodak DCS460c.
More info: https://www.digitalkameramuseum.de/en/cameras/item/kodak-dcs-460
Camera image: https://productz.com/en/kodak-dcs460/p/9BM2

## Slide 34
Reconstructed radiance map

## Slide 35: Results: Color Film
Kodak Gold ASA 100, PhotoCD
Notes: 14

## Slide 36: Recovered Response Curves
Red
Green
RGB
Blue
Note: we recover for each of RGB
Notes: 15

## Slide 37: The Radiance Map
= Radiance map (averaged across RGB)
False color map to show relative range of output
Notes: 17
James note: this may not strictly be an average (a mean), and some weighting of the different channels may have occurred.

## Slide 38: How do we store this?

## Slide 39: Portable FloatMap (.pfm)
12 bytes per pixel, 4 for each channel
sign
exponent
mantissa
PF
768 512
1
<binary image data>
Floating Point TIFF similar
Text header similar to Jeff Poskanzer’s .ppm image format:

## Slide 40: Radiance Format (.pic, .hdr)
(145, 215, 87, 149) =
(145, 215, 87) * 2^(149-128) =
(1190000, 1760000, 713000)
Red Green Blue Exponent
32 bits / pixel
(145, 215, 87, 103) =
(145, 215, 87) * 2^(103-128) =
(0.00000432, 0.00000641, 0.00000259)
Ward, Greg. "Real Pixels," in Graphics Gems IV, edited by James Arvo, Academic Press, 1994

## Slide 41: ILM’s OpenEXR (.exr)
6 bytes per pixel, 2 for each channel, compressed
sign
exponent
mantissa
Several lossless compression options, 2:1 typical
Compatible with the “half” datatype in NVidia's Cg
Supported natively on GeForce FX and Quadro FX
Available at http://www.openexr.net/
5 bit exponent
10 bit mantissa

## Slide 42: Now What?
= Radiance map (averaged across RGB)
Notes: 17

## Slide 43: Tone Mapping
10-6
106
10-6
106
Real World
Ray Traced
World (Radiance)
Display/
Printer
0 to 255
High dynamic range
How can we do this?
  Linear scaling?, thresholding? Suggestions?

## Slide 44: The Radiance Map
Linearly scaled to
display device
Notes: 16

## Slide 45: Simple Global Operator
Compression curve needs to
  Bring everything within range
  Leave dark areas alone
In other words
  Asymptote at 255
  Derivative of 1 at 0

## Slide 46: Global Operator (Reinhard et al.)
= Radiance map
Notes: Reinhard et al., Photographic tone reproduction for digital images
SIGGRAPH 2002
https://doi.org/10.1145/566570.566575
Note that Reinhard et al. use luminance instead of radiance, and use in their notation for a luminance map (not and a radiance map). For our purposes, we will treat them as the same.
Reinhard et al., Photographic tone reproduction for digital images
SIGGRAPH 2002
https://doi.org/10.1145/566570.566575
Note that Reinhard et al. use luminance instead of radiance, and use 𝐿 in their notation for a luminance map (not 𝐸 and a radiance map). For our purposes, we will treat them as the same.

## Slide 47: Global Operator Results

## Slide 48
Darkest 0.1% scaled
to display device
Reinhart Operator

## Slide 49: What do we see?
Vs.

## Slide 50: Issues with multi-exposure HDR
Scene and camera need to be static
Camera sensors are getting better and better
Display devices are fairly limited anyway (although getting better).

## Slide 51: High-dynamic range on smartphones
[https://techcrunch.com/2018/09/12/the-7-most-egregious-fibs-apple-told-about-the-iphone-xs-camera-today/]
Apple, iPhone X/XS/XR
“We have a brand new feature we call smart HDR”
Always-on bracketed exposures:
Even when you aren’t taking pictures, the camera saves to a buffer with varying exposures.
Use that data to do HDR

## Slide 52: Google Pixel phones (2016)
Notes: https://ai.googleblog.com/2018/02/introducing-hdr-burst-photography.html

## Slide 53
Notes: Samuel W. Hasinoff, Dillon Sharlet, Ryan Geiss, Andrew Adams, Jonathan T. Barron, Florian Kainz, Jiawen Chen, and Marc Levoy. 2016. Burst photography for high dynamic range and low-light imaging on mobile cameras. ACM Trans. Graph. 35, 6, Article 192 (November 2016), 12 pages. DOI: https://doi.org/10.1145/2980179.2980254

## Slide 54: Ghosting
Notes: Automatic Noise Modeling for Ghost-free HDR Reconstruction
Miguel Granados, Kwang In Kim, James Tompkin, Christian Theobalt
ACM Transactions on Graphics (SIGGRAPH Asia 2013)
Project webpage

## Slide 55: Tone-mapped HDR as a look
[http://pancake-ninja.blogspot.com/2011/06/hdr-bus.html]

## Slide 56: Local tone mapping / bilateral filter
Flickr user mapgoblin
Notes: http://www.flickr.com/photos/mapgoblin/142350388/

## Slide 57: Recovering HDR radiance maps for the project
Additional slides not shown in class
[James Hays]

## Slide 58: Debevec and Malik 1997
• 3
• 1
• 2
Dt = 1 sec
• 3
• 1
• 2
Dt = 1/16 sec
• 3
• 1
• 2
Dt = 4 sec
• 3
• 1
• 2
Dt = 1/64 sec
Image series
• 3
• 1
• 2
Dt = 1/4 sec
Pixel Value Z = f(Exposure)
Pixel Value Z = f(Radiance x Dt)
g(Pixel Value Z) = ln(Radiance) + ln(Dt)
f -1(Pixel Value Z) = Radiance x Dt
Notes: 10
Assumption – f is monotonic and invertible. Probably true.

## Slide 59
Dtj = 1/16 sec
• 3
• 1
• 2
Dtj = 1/64 sec
Dtj = 1/4 sec
Image Sequence
• 3
• 1
• 2
• 3
• 1
• 2
For each pixel site in each image , want:
is the unknown discrete inverse response function. We will solve for each color channel independently.
is the known (but noisy) pixel value from 0 to 255 for location in image .
is the unknown radiance at location .
is the known exposure time, e.g. 1/16, 1/128, for image
Equation 2 in Debevec
Notes: 10

## Slide 60
Dtj = 1/16 sec
• 3
• 1
• 2
Dtj = 1/64 sec
Dtj = 1/4 sec
Image Sequence
• 3
• 1
• 2
• 3
• 1
• 2
-4.9875
-4.7250
-4.4628
-4.2095
-3.9744
…
2.0197
2.0654
2.1149
2.1686
2.2255
Example of what g(Zij) looks like
256 unknowns
Notes: 10

## Slide 61
Dtj = 1/16 sec
• 3
• 1
• 2
Dtj = 1/64 sec
Dtj = 1/4 sec
Image Sequence
• 3
• 1
• 2
• 3
• 1
• 2
-4.9875
-4.7250
-4.4628
-4.2095
-3.9744
…
2.0197
2.0654
2.1149
2.1686
2.2255
Example of what g(Zij) looks like
256 unknowns
Notes: 10

## Slide 62
Dtj = 1/16 sec
• 3
• 1
• 2
Dtj = 1/64 sec
Dtj = 1/4 sec
Image Sequence
• 3
• 1
• 2
• 3
• 1
• 2
-4.9875
-4.7250
-4.4628
-4.2095
-3.9744
…
2.0197
2.0654
2.1149
2.1686
2.2255
We expect g() to vary smoothly
Example of what g(Zij) looks like
256 unknowns
Notes: 10

## Slide 63
Dtj = 1/16 sec
• 3
• 1
• 2
Dtj = 1/64 sec
Dtj = 1/4 sec
Image Sequence
• 3
• 1
• 2
• 3
• 1
• 2
-4.9875
-4.7250
-4.4628
-4.2095
-3.9744
…
2.0197
2.0654
2.1149
2.1686
2.2255
We expect g() to vary smoothly
Add constraints on second derivative of g()
Example of what g(Zij) looks like
256 unknowns
Notes: 10

## Slide 64
Dtj = 1/16 sec
• 3
• 1
• 2
Dtj = 1/64 sec
Dtj = 1/4 sec
Image Sequence
• 3
• 1
• 2
• 3
• 1
• 2
-4.9875
-4.7250
-4.4628
-4.2095
-3.9744
…
2.0197
2.0654
2.1149
2.1686
2.2255
Example form of g(Zij)
256 unknowns
We expect g() to vary smoothly
…
254 equations
num_samples * num_images equations
Lock down one point in g()
Notes: 10

## Slide 65
Dtj = 1/16 sec
• 3
• 1
• 2
Dtj = 1/64 sec
Dtj = 1/4 sec
Image Sequence
• 3
• 1
• 2
• 3
• 1
• 2
…
254 equations
num_samples * num_images equations
Lock down one point in g()
We can’t trust all of these values
Weight each equation by trustworthiness
Notes: 10

## Slide 66
Dtj = 1/16 sec
• 3
• 1
• 2
Dtj = 1/64 sec
Dtj = 1/4 sec
Image Sequence
• 3
• 1
• 2
• 3
• 1
• 2
…
We can’t trust all of these values
Weight each equation by trustworthiness
Notes: 10

## Slide 67
…
How do we convert this to Ax=b form?
254 equations
num_samples * num_images equations
1 equation
A x = b
1
254
num_samples * num_images
256
256 + num_samples
1
1
num_samples
x = A\b
non-zero entries
MATLAB
Python
numpy.linalg.lstsq(A,b)
Notes: 10
https://numpy.org/doc/stable/reference/generated/numpy.linalg.lstsq.html

## Slide 68: Exposure Fusion
Tom Mertens1 Jan Kautz2 Frank Van Reeth1
1 EDM - Hasselt University
2University College London, UK
https://dl.acm.org/citation.cfm?id=1338586 / https://mericam.github.io/
Notes: Hi, welcome everybody.
My name is Tom Mertens, and I am gonna talk about Exposure Fusion, which is a research project I carried out together with Jan Kautz from UCL and Frank Van Reeth from Hasselt University.

## Slide 69
underexposed
overexposed
both
!
!
!
!
Notes: Exposure fusion deals with the following problem.
So, photographers are often troubled by this here: a picture is under or overexposed.
This usually happens because the dynamic range of intensities found in the scene is too high to be captured by the camera.
This problem can be avoided by manipulating the exposure settings, like shutter speed and aperture, but this is sometimes impossible, and you’ll get both under and overexposed parts.

## Slide 70
Multi-exposure sequence
High Dynamic Range photography
Notes: Now, you can simply take differently exposed images from the same vantage point, in order to create a good image that does not have these exposure artifacts, and this lies at the basis of high dynamic range photography.
Our technique deals with the same kind of input, but we take a different approach.

## Slide 71: HDR Photography
HDR assembly: LDRs  HDR
  [Mann and Picard, IS&T ‘95]
  [Debevec and Malik, SIGGRAPH ‘97]
Tone mapping: HDR  LDR
  [Durand and Dorsey, SIGGRAPH ‘02]
  [Reinhard et al., SIGGRAPH ‘02]
  [Fattal et al., SIGGRAPH ‘02]
  [Li et al., SIGGRAPH ‘05]
  [Lischinski et al., SIGGRAPH ‘06]
Exposure Fusion: LDRs  LDR
Notes: We’ve seen a fair amount of work in the past decade on this topic
First, people have come up with ways to take multiple LDR exposures, and assembled them into a HDR image.
But this is not enough. Not only the camera, but also display devices like most monitors, do not have the capability of dealing with HDR content.
So this is why we apply tone mapping first, which is a process that maps HDR image back to LDR, in a perceptually motivated fashion. This basically means that the resulting LDR image is perceived by a human as if it still were a HDR image, it still has to look good and artifact free.
Exposure fusion basically does the same thing, but it skips the part where we compute a HDR image.
So why do this?

## Slide 72
Multi-exposure
Assembly
Response curve
calibration
Tone
mapping
display
bilateral
gradient
…
High Dynamic Range photography
Notes: Well, let’s look at the HDR photography pipeline. It’s not a simple process.
First of all, your camera’s response curve has to be calibrated. This is not so bad, but it puts an extra burden on the user, especially if she or he does not know much about HDR photography.
After the images have been assembled into an HDR image, you need to pick on of the many tone mapping operators, and then possibly tweak it in order to have the desired result. This can also be a very tedious process for a novice user.
Exposure fusion is much simpler. Not only is easier to understand, but it has less parameters to tweak, easy to implement, and it also quite efficient in terms of computation.

## Slide 73
display
Exposure fusion
Multi-exposure
Multi-exposure
Assembly
Response curve
calibration
Tone
mapping
display
bilateral
gradient
…
High Dynamic Range photography

## Slide 74
Idea: fuse multi-exposure sequence
Notes: So here’s the basic idea behind our approach.
Notice how in this multi-exposure sequence you can always find “good parts”, meaning pixels that are already well-exposed.
The idea now is to detect those regions, and fuse them into a single, good-looking image.
And here a result of our approach.

## Slide 75: Image Fusion
Applications
  Extended depth-of-field
    [Ogden et al. ‘85]
    [Agarwala et al., SIGGRAPH ‘04]
  Multi-sensor photography
    [Burt et al. ‘93]
  Non-photorealistic video
    [Raskar et al., NPAR ‘04]
Exposure Fusion
  Manual (Photoshop)
  Image pyramid [Burt et al. ‘93]
Extended DOF
Multisensor: IR + visible
Notes: So we want to fuse images, and this quite related to the more general concept of image fusion – people have looked at this before for other applications.
For instance, in a situation where you’re stuck with a shallow DOF, like in macrophotography, you can focus on different parts of your subject and then fuse those image into a image with extended depth-of-field.
You can also fuse image that were shot with different sensors. For instance you can combine a regular photograph with an infrared photo.
The basic idea of exposure fusion is actually not new, because people have done something similar before. In fact, you can use photoshop by manually blending between the different exposures. Of course this is quite tedious and labour-intensive
Burt et al. have suggested fusing multiple exposures, but they did this in a more general framework for image fusion. In our work however, we have specifically designed a fusion technique, specifically for this particular case.
But let’s take a closer look at this approach…

## Slide 76: Pyramid Fusion
[Ogden et al. ’85, Burt et al. ‘93]
Notes: Here are 2 images you want to fuse.

## Slide 77: Pyramid Fusion
abs
max
reconstruct
[Ogden et al. ’85, Burt et al. ‘93]
Pyramid decomposition
“multi-scale edge filter”
-1 0 1
Notes: The idea is that the fusion takes place in a pyramid decomposition, so I’m gonna refer to this method as “pyramid fusion”.
For now, it doesn’t really matter what pyramid to use: it could be a Laplacian or steerable pyramid. But intuitively, this decomposition basically acts like a edge filter, and it does so at multiple scales.
Not only can you build a pyramid, but you can convert back to your image, after you changed its content.
Here, we fuse the image by computing a pyramid by selecting for each pixel the pixel that has the maximum absolute value. So what basically happens is that you consolidate all your details (or edges) into a single image.
We then reconstruct the image, and we’re done.

## Slide 78
Pyramid Fusion
Exposure fusion
Notes: Here’s a result of this approach.
You can see that it produces an okay result, but unfortunately the colors are not the same anymore, and some parts still remain dark.
Our technique does not suffer from this problem, as it only selects and blend the best parts of the image, and does not change anything else. Whereas, pyramid fusion may significantly alter the image by only trying to maximize the amount of details.

## Slide 79
Multi-exposure
Challenges:
Good weights
Good blending
Weight
X
+
Notes: Now let’s look at our approach.
Here’s your multi-exposure sequence. For each pixel you’re gonna compute a weight map, which will indicate which pixels we want to keep.
Then, we blend this selection into the final result.
So there are 2 things we need to do, first, find good weights, and second come up with a good blending strategy.

## Slide 80
Notes: Let’s look at the weights first

## Slide 81
saturation
well-exposedness
contrast
Notes: Let’s look at the weights first
We compute 3 measure that will help us to select pixels, which we call contrast, saturation and well-exposedness.

## Slide 82
saturation
well-exposedness
contrast
weight = st_dev(R,G,B)
saturation
0 1 0
1 -4 1
0 1 0
weight = | h * image |,
h =
contrast
intensity
1
0
1
weight
f(i)
weight = f(intensity)
well-exposedness
Notes: Contrast is basically an edge detector, and it give more weight where details are. The idea behind this, is that over or underexposed parts contain less detail, whereas you have most detail in wellexposed regions.
Saturation is a measure of how bright a color is. Again, the reasoning behind this, is that as a pixel becomes overexposed, its color also becomes less saturated. Also, saturated colors just look better, it’s a desirable quality.
Finally, we compute a measure called well-exposedness, which simply give more weight to pixel that have an intensity close to .5, whereas intensities close to 0 will be considered underexposed, and close to 1 are overexposed.

## Slide 83
normalized
select or combine
saturation
well-exposedness
contrast
Notes: Now, we compute a single weight map by either selecting one of the measures, or combining them using multiplication.
This is the only part where the user has to provide input: he or she has to select a measure. Or you could also just select all the measures by default, if the user doesn’t care, which would already produce good results.
Finally, we normalize the weight map, by making the weights sum to one.

## Slide 84
Multi-resolution blending
Naïve blending
Exposures
Weights
Notes: Now that we have our weight, we could simple linearly blend between the exposures. However, this doesn’t yield the desired result.
Because the intensities very so wildly among the different images, and the weight maps may contain very sharp transitions, you’ll introduce spurious edges, edges that weren’t there before.
So instead, we perform the blending in a multi-resolution fashion, which I’ll explain in the next couple of slides.

## Slide 85
[Burt and Adelson, ACM TOG ‘83]
Multi-resolution Blending
Notes: This idea of multi-resolution blending is based on work by Burt and Adelson, who developed this technique for seamless cloning and mosaicking.
It’s much like the work on poisson image editing and gradient domain techniques, but simpler. It does the blending using a pyramid decomposition.

## Slide 86: Multi-Resolution Blending
x
Notes: Let’s see how this works in our context.

## Slide 87
[Burt and Adelson, ACM TOG ‘83]
Multi-Resolution Blending
Laplacian pyramid
Gaussian pyramid
+
x
reconstruct
Notes: We compute a pyramid of the input images, and alongside this, we have a Gaussian pyramid of the weight maps. This basically contains downsampled versions of the weights.
Now for each pyramid level, we will perform regular blending, giving us a new pyramid, and we reconstruct it to get the result.

## Slide 88
intensity
weight
blended
Laplacian
pyramid
Notes: Okay, so here’s a comparison again of regular and multiresolution blending, and the improvement is quite dramatic actually, but you might wonder why exactly.
Let me try to illustrate this with a simple example.
Let’s say we have 2 input images, an underexposed one and an overexposed.
I took a scanline, and plotted it here. I also have the corresponding weights here.
Now, because the weight map contains abrupt changes, it will introduce spurious edges in the result, as shown here.
The multiresolution approach does the blending in the Laplacian pyramid.
Now, remember that this acts as a edge filter, so wherever you have smooth regions, you’ll have a value close to zero, and the blending will have little effect.
But this is also exactly where you don’t want to introduce new edges. It’ll only have effect when there was already an edge.

## Slide 89: Results
Notes: Let’s turn to the results now.

## Slide 90
Notes: So here’s a typical bracketed sequence that a photographer would take: you’ll have a under and overexposed image, and one in between.
And below is our result.

## Slide 91
Notes: Here’s another example

## Slide 92
Exposure fusion
Middle exposure
Notes: Let’s see how it compares to LDR. Here’s the middle exposure in the bracketed sequence. And you see that it pays off to take into account those extra images.

## Slide 93
Exposure fusion
Mean image
Notes: It’s also interesting to compare to the most trivial form of exposure fusion, namely to take the average image. But as you can see, this results in a very washed out image, and details are lost.

## Slide 94
contrast + saturation
Well-exposedness
Notes: By selecting different measures, you also get different results. Notice how the wellexposedness measure creates a more surreal result here, while a combination of contrast and saturation produces a more conservative image.

## Slide 95
Single exposure
Exposure fusion
Pyramid fusion
[Ogden85; Burt93]
Notes: Here’s another comparison with the most relevant work on general image fusion, which I mentioned earlier.
Again, you see that our method reproduces the colors better, and does not look too dark.

## Slide 96
[Li et al. ‘05]
[Durand and Dorsey ‘02]
[Reinhard et al. ‘02]
Exposure Fusion
Notes: It’s also interesting to compare with tone mapping, and here are a couple of examples. Now, this is more of a informal comparison, because the interpretation of these results can be somewhat subjective, as was mentioned in the previous talk.
As you can see, our technique produces fairly competitive results.

## Slide 97: Flash/No Flash
Ambient
Flash
Exposure Fusion
Also see: [Eisemann and Durand ’04, Petschnigg et al. ’04, Agrawal et al. ’05]
Notes: So here’s an interesting side-result of our approach. Exposure fusion is somewhat like a black box approach, so you can feed it anything you want. So we found that it also works with flash/no flash pairs, an idea that has been explored by these researchers as well.
Now I’m not claiming that we’re doing a better job here, but our method is able to produce some interesting results on this type of input.

## Slide 98: Conclusion
Simple, fast and flexible
Pixel selection + blend
  perceptual measures
  multi-resolution blending
Few parameters to tweak
Not physically-based
Future work
  More measures
  More applications
  Real-time GPU implementation for video
contrast
saturation
well-exposedness

## Slide 99: Acknowledgments
Photos:
  Min Kim
  Jesse Levinson
  Jacques Joffre
  Amit Agrawal
European Regional Development Fund
http://research.edm.uhasselt/~tmertens
  Matlab code

## Slide 100
IR
visible
Exposure fusion

## Slide 101
Middle exposure
Exposure fusion
Notes: So let’s see how much better we’re doing than a regular exposure.
You see here that our result contains more details, especially for the clouds.

## Slide 102
Mean Image
Exposure fusion
Notes: It’s also interesting to compare to the most trivial way of doing exposure fusion, namely just taking the average of the input images. And you see that again we preserve more detail.

## Slide 104: Maui Sunset
Mean image
Exposure fusion
-2 stops
+2 stops

## Slide 105: Maui Sunset
Middle exposure
Exposure fusion
-2 stops
+2 stops

## Slide 106
Exposure fusion
Middle image
Mean image

## Slide 107: Bibliografía
R. Szeliski, Computer Vision, Springer 2010, Capítulo 10.2
Paul E. Debevec and Jitendra Malik. “Recovering High Dynamic Range Radiance Maps from Photographs”, in SIGGRAPH 97, 1997.
Erik Reinhard, Michael Stark, Peter Shirley, and James Ferwerda, “Photographic tone reproduction for digital images”, in SIGGRAPH 02, 2002.
Tom Mertens, Jan Kautz and Frank Van Reeth, “Exposure Fusion”, in proceedings of Pacific Graphics, 2007